Car ( tow vehicle side)

1

white
10
common ground- same on trailer
2
blue
12
electric brake- to yellow on trailer
3
green
14
tail/running lights to green on trailer
4
black
10
battery charge (+) to blue on trailer
5
red
14
left turn/stop – to red on trailer
6
brown
14
right turn/stop to brown on trailer
7
yellow
14
auxiliary/back up- to black on trailer

# trailer side
NEW CORD (yellow) --> TRAILER (black) : aux/back up

NEW CORD (black) --> TRAILER (blue) : charge line

NEW CORD (blue) --> TRAILER (yellow) : brake

# 7 Way RV Connector

Pictured below is the Pollak 7 way connector, which is the connector style in most common use on RV trailers and is becoming increasingly popular on horse and utility trailers. This connector is also manufactured by the Theodore Bargman Company and there are also some generics around. They are supposed to be interchangeable and the wiring color code is maintained among the various brands.

As you can see in the illustration below the back side of the connector body is labeled at each terminal. The labels are listed below with the function assigned to that pin.

On the tow vehicle side with the exception of 96-98 Ford and Dodge pickups and SUV's with factory installed trailer wiring, wire color alone should not be relied on, always test and match the function to the appropriate terminal.

On the trailer side RV's for the most part are wired to match the connector colors. Any plug that has been changed or extended, along with horse and utility trailers should be tested when replacing for any reason to be sure the function matches the terminal.

It should be noted below that the center terminal is labeled as an auxiliary circuit, most commonly used for backup lights not a ground terminal as many try to make it.

Also after the connector diagrams find more information on wire colors used by GM, Ford, and Dodge.

| Wiring Code 7 way Car End |
| --- |
| # | Color | Gage | Circuit Function | connector interior |
| 1 | white | 10 | common ground |  |
| 2 | blue | 12 | electric brake |  |
| 3 | green | 14 | tail/running lights |  |
| 4 | black | 10 | battery charge (+) |  |
| 5 | red | 14 | left turn/stop |  |
| 6 | brown | 14 | right turn/stop |  |
| 7 | yellow | 14 | auxiliary/back up |  |
| NOTE: #7 is the center terminal and currently is most commonly used for backup lights. |

| Wiring Code 7 way Trailer End |
| --- |
| # | Color | Gage | Circuit Function | connector interior |
| 1 | white | 10 | common ground |  |
| 2 | blue | 12 | electric brake |  |
| 3 | green | 14 | tail/running lights |  |
| 4 | black | 10 | battery charge (+) |  |
| 5 | red | 14 | left turn/stop |  |
| 6 | brown | 14 | right turn/stop |  |
| 7 | yellow | 14 | auxiliary/back up |  |
| NOTE: #7 is the center terminal and currently is most commonly used for backup lights. |

Click for 6 way connector wiring.

This chart should be used as a general guide only, you should always test before connecting your wiring.

This chart also may not be accurate for vehicles with factory installed trailer harnesses. In past 2-3 years manufacturers have begun to match the wire colors to the code for the common 7 way RV connector. More on that after the chart.

| Caution if your vehicle has a diagnostic indicator that tells you when a lamp is burned out or not functioning, you may need special wiring adapters and testers. Not using these adapters may cause damage to the vehicle wiring or computer. |
| --- |
| function | GM | Ford | Chrysler |
| left turn & brake lights | yellow | lt green w/orange stripe | dk green |
| right turn & brake lights | dk green | orange w/blue stripe | brown |
| tail lights | brown | brown | black or black w/yellow stripe |
| back up lights | lt green | black w/pink stripe | violet |
| ground see note 1 | black | black or grey | black |
| In addition to the above some cars and trucks have a separate light for the brake light, most commonly identified by amber turn lenses in the rear. Chrysler and Jeep may have the separate light and use red lenses. If you have this type of wiring a converter is required. |
| brake light | lt blue or pink | red w/green stripe | white |
| Note 1: We recommend attaching the trailer harness ground directly to the frame or a solidly attached sheet metal part, using a screw or bolt. The single most common cause of trailer lighting problems is a poor ground on the tow vehicle or trailer. |

The common flat 4 wire connector used on boat, snowmobile, and light utility trailers most commonly uses the following code.

| Flat 4 wiring code |
| --- |
| white | ground |
| yellow | left turn/brake light |
| green | right turn/brake light |
| brown | tail |

#### Ford tow vehicles with the Factory Tow Package Brake Connector

Ford vehicles with this package are equipped with a 20 amp fused power line which is insufficient for 3 & 4 axle (6 or 8 brake) applications. For 3 & 4 axle (6 or 8 brake) applications a separate power wire should be installed directly from the battery positive to the brake control and should include an inline 30 amp auto reset circuit breaker.

| Ford brake control connector wiring harness color code for factory supplied harness |
| --- |
| Ford supplied brake control harness | Tekonsha brake control wires All electronic models | function |
| pink | black | +12 volt |
| red | red | stoplight |
| white | white | ground |
| dark blue | blue | trailer brakes |
| brown | not used |  |
| NOTE: The above applies only to the Ford factory supplied harness, if using Tekonsha harness #3035, the harness colors match the brake control |