Solar Gray-Water Evaporation Pond for Black Rock City

This thing really works, but if you use water like they do in Las Vegas… forget it!

4’x8’ or 32 sq ft

(sized for 2 to 4 people w/moderate use)

| Materials: (no screws required) 2ea. 2x4x8’ utility grade lumber 2ea. 2x4x4’ “ “ “ 2ea. 6’x10’ 6 mil black plastic (1 is a spare) 4ea. #4 (½”) x 3’ rebar 4ea. ½” x 5’ Sch. 40 PVC pipe, white 1ea. roll of flagging ribbon, bright color 1ea. roll of HD duct tape 4ea. Solar path lights 5 gal plastic bucket(s) w/lid(s) 6ea. paint strainers, gallon size Windshield squeegee w/bug mesh 30 gal HD trash bag Disposable gloves *********************************** Tools: HD stapler w/ 5/16” staples Sledgehammer (for rebar) ViseGrip (to help pull rebar) *********************************** Note: ~Use moderate amounts of h2o & low fragrance biodegradable soap and shampoo, (Dr. Bronner’s...?); take a sponge bath everyday w/baby wipes instead of a shower! ~Wipe food and grease from dishes w/paper towel before washing. ~Duh… don’t pee in your gray water! ~Wind may lift 6 mil, so place something heavy like jugs of h2o in each corner & in the middle. | Construction: (in an out-of-the-way place) »Sweep playa for v/smooth surface »Form rectangle frame w/2x4’s, on edge »Tape outside corners w/12” strips, 3 layers thick, then staple tape to frame »Drape 6 mil over frame, pull flat, tuck into corners, fold over edge and staple to outside of frame, tuck excess under frame »At each outside corner pound in rebar about 8” then slide PVC pipe over it. »Run flagging ribbon from pipe to pipe »Place solar light at each corner *********************************** Use Instructions: »Handle gray-water, etc w/gloves. »Add strained gray-water to pond. »Maintain pond level <1” but <½” is best. »Squeegee 6 mil w/bug mesh if dust-mud collects. »Discontinue adding water a couple days before exodus; put last few days in holding tank or buckets w/lids for off playa disposal. »Dispose of all used staples & tape w/care »Bundle used 6 mil into 30 gal trash bag for off playa disposal. *********************************** ~If it rains cover pond w/spare 6 mil. ~Leaks?.. dry then duct tape and/or place a full h2o jug on a scrap of 6 mil. |
| --- | --- |

See: http://www.burningman.com/preparation/event_survival/grey_water.html